## Slide 1: PIM Architecture
B815133 이성현
전자전기공학부
Source: Optimizing Weight Mapping and Data Flow for Convolutional Neural Networks on RRAM
2024년 9월 9일

## Slide 2: 목차
Review SRAM accelerator
Partition Scheme
A Novel mapping method
Data Flow to Maximize IFM Reuse
PIM Architecture

## Slide 3: Review SRAM accelerator
Source: Partition SRAM and RRAM based Synaptic Arrays for Neuro-inspired Computing
Multiple SRAM cells(m cells) as one synaptic weight element along the row
The read(weighted sum) and write(weight update) operation are row-by-row based
One adder and register pair for row-by-row summation
In write operation, all the cells on the row can be updated at the same time

## Slide 4: Review SRAM accelerator(Example)
IN[1]
Layer i
IN[2]
O[1]
Layer i+1
O[2]
O[3]
O[4]
n =4
W11
W12
Precharger
Write Driver
WL Decoder
m bits as 1 element
W11
W12
IN[1]
IN[2]
IN[1]*W11+IN[2]*W12=O[1]
S/A
S/A
Adder
Register
W41
W42
Adder
Register
IN[2]*W12
IN[1]*W11
S/A
S/A
IN[1]*W41
IN[2]*W42
O[1]
O[4]

## Slide 5: Partition Scheme
Source: Partition SRAM and RRAM based Synaptic Arrays for Neuro-inspired Computing
Partition the large array core into NxN small arrays in a hierarchical fashion
In write operation, weight elements in different sub-arrays can be updated in parallel
In read operation, they are computed in parallel but the results from all sub-arrays must be collected and summed up
Use multi-stage adders and registers to obtain the final weighted sum

## Slide 6: Partition Scheme(Example)
Q<0~n>
Q<0>
Q<1>
Q<n>
<0>
Q<0>=IN[1]*W11
<0>=IN[2]*W12
O[1]=Q<0>+ <0>
Q<1>=IN[1]*W21
<1>=IN[2]*W22
O[2]=Q<1>+ <1>
<1>
<n>
<0~n>
O[1~n]

## Slide 7: A basic mapping method
One 3D kernel with size KxKxD could be unrolled to a long vertical column which length equals to KxKxD
N vertical columns in total
To get the OFMs, at first cycle, a part of IFMs(dark blue cube) will be multiplied with each 3D kernels
The result will be first elements in every OFM(light green row in size 1x1xN)

## Slide 8: A Novel Weight Mapping Method
Map the weights at different spatial location of each kernel into different sub-matrices
KxK sub-matrices are needed for the KxK kernels
Each sub-matrix can be represented by a group of sub-arrays

## Slide 9: Data Flow to Maximize IFM Reuse
Processing element(PE) consists of a group of sub-arrays with the necessary inputs, output buffers, accumulation modules and L1 Buffer
Maximize the reuse of input data
PE

## Slide 10: PIM Architecture
PIM contains multiple tiles, accumulation units, pooling and activation units, L3 buffer and the global control
Tile contains multiple PEs with routers and L2 buffer
Conclusion
A small amount of bits will be visited in buffers
Efficient latency and energy consumption